## Slide 1: High level overview of the topic
Develop algorithm to recognize human movement such as walking, direction of motion, usage of the area, using time synchronized PIR sensor data.
Show the effect, unsynchronized data has on the developed algorithm .
Implement clock synchronization of each node with a global clock and improve the accuracy of the algorithm.

## Slide 2: What has been done so far
Getting to know the existing test bench.
Interface of the Memsic sensors with the PC.
Interface of the eZ430-RF2500(TI) sensor with the PC.
Data collected from the existing test bench.
Conclusion: Sampling time is high for the existing test bench.
Preparing the TI sensor to collect data.

## Slide 3: Testbed with eZ430-RF2500
Sampling rate has been set to 100ms
32 samples are collected together and packed into a packet and then transmitted every 3.2s. (4 bytes)
MAC ID for each node(4 bytes can be reduced)
Time stamp at which the packet is created. The time stamp is the local time stamp at the node.(2 bytes)
Packet number(1 byte).
Maximum payload size 20bytes.

## Slide 4: Time synchronization for initial data collection.
A crude method of synchronizing the nodes for initial data collection.
AP broadcasts a packet to all the nodes to start the timer.
The packet is transmitted several time(2) from the AP to ensure all nodes receive the packet.
At the nodes the packets are transmitted once every 3.2ms.
3.2 ms are divided in to 32 slots of 100ms. Each nodes are assigned 1 slot randomly. This increased the efficiency of transmission.
Trying to reset the the node through software to avoid manual removal of the nodes from the ceiling. Works when there are 2 or 3 nodes.

## Slide 5: Road map
January – Finish setting up the test bench and collect data. Start with analysis of data.
February – Literature survey continued and develop algorithm to extract information from the PIR sensor data.
March – Introduce artificial delay to the collected sensor data or collect unsynchronized data from the sensor. Check the efficiency of the algorithm and see the effects of having unsynchronized data.
April and May- Time synchronization: literature survey and implementing it on the sensor nodes. Testing it.
June- Evaluating the performance of the proposed solution. Improving the algorithm if required.
July and August: Writing thesis.